## Slide 1: TOOL PATH PLANNING FOR FACE MILLING OF 3-D SURFACE
Presented by: Aayushi Verma
Roll No. : 18ME02034
Guided by: Dr. Gaurav Bartarya
School of Mechanical Sciences,
IIT Bhubaneswar

## Slide 2: Tessellated representation
To fabricate any design, the 3-D model (surface or solid) has to be transferred to STL (Standard Tessellation Language) format.
The STL file format is generated using a tessellation process, which generates triangles to represent the CAD model.
The STL model is mathematically sliced by intersecting it with horizontal planes. Each slice represents a cross-section data for the part.

## Slide 3
Figure 1: An object and its tessellated representation

## Slide 4
Fig 2- : STL File and description of ASCII representation format
These triangles are described by a set of X, Y and Z coordinates for each of
three vertices, and a unit normal vector to indicate which side of the
triangle contains the mass.
STL file can be in ASCII or in binary format.

## Slide 5: OBJECTIVE
To develop a tool path plan using STL format of 3D object by slicing the model.

## Slide 6: Reading STL file
START
Reading first line from STL
file using fgetl and save it to
‘a1’
Set values to ‘fn’ and ‘v’ as
‘Facet Normal’ and ‘Vertex’
Open STL file using
fopen
While loop Checking that is there a character in ‘a1’
if
Finding whether
stored ‘fn’ value
is in ‘a1’ or Not
A

## Slide 7
A
Saving the integer values from line to
a variable ‘a’ which is further stack up
in ‘normal’ array
Saving the integer values from line to
a variable ‘a’ which is further stack up
in ‘vertex’ array
elseif
Finding whether
stored ‘v’ value
is in ‘a1’ or Not
Reading next line from STL
file using fgets and save it to
‘a1’
END
Close the file using fclose(FileID)

## Slide 8: Slicing the model
Find the Cutting Plan (Zc)
The program scans STL file, picks the Z-coordinate of all the triangle, compare, and find the top, the bottom of the geometric (Zmin, Zmax ), add the slice thickness to Zmin.
Zc = Zmin + slice thickness
Find the Facets that intersect with the Cutting Plan
The program scans STL file to pick one triangle at a time, the Z-coordinate of its three vertices compared with the Z-height of the current plane,
Zmin <= Zc <= Zmax , Zmin, Zmax are in one triangle

## Slide 9
Saving three consecutive co-ordinate having row index as i-2,i-1,i and repeating first
co-ordinate and save it to array ‘a’
Find u using following equation :-
u = (Zc-Zj)/(Z(j+1)-Zj)
For j=1:size(a)-1
For i=1:m
If mod(i,3)==0
A
If Zc>Zmax
START
Zc=Zmin
End of program
Yes
No
Yes
No
B

## Slide 10
A
Find x_inter, y_inter which are intersection points, using following equation:-
x_inter = Xi+u*(X(i+1)-Xi)
y_inter = Yi+u*(Y(i+1)-Yi)
Save all x-y intersection ‘points ‘ variable and continue to find intersection points for next triangle
END
If u>=0 && u<=1
Zc=Zc + slice_thickness
Yes
No
B
Fig. 3- Three vertices of one triangle and the
intersection points

## Slide 11
Fig. 4- Intersection points
Fig. 3- The possible cases for triangle-plane slicing

## Slide 12
Find u using following equation :-
u = (Yi-Y0)/(Y1-Y0)
For i=1:m
If Yi>Ymax
START
Yi=Ymin
End of program
Yes
Yes
No
Tool Path Algorithm
Let <L1{(X0,Y0),(X1,Y1)},L2{(X0,Y0),(X1,Y1)} ………..Lm{(X0,Y0),(X1,Y1)}> be array of
intersecting line segments.
If u>=0 && u<=1
Compute: - x= X0+u*(X1-X0)
And store x value in ‘p’ array
A
B

## Slide 13
A
Append xmin at front and xmax at last of the array ‘p’
Yes
No
B
Sort array ‘p’ and remove duplicate points
If mod(j,2)==0
Tool cutting OFF/Stop
Yi=Yi + stepsize
For j=1:size(p)
Tool cutting ON/Start

## Slide 14
Fig..5- Zc=zmin
Fig..6- Zc=zmax

## Slide 15
b) Zc=maxz
c) Zc=maxz-10
d) Zc=maxz-30
e) Zc=maxz-50
Fig.7 a) 3D model of bracket

## Slide 16
c) Zc=maxz-10
d) Zc=maxz-30
b) Zc=maxz
e) Zc=maxz-50
Fig. 8 a) 3D model of bracket

## Slide 17
b) Zc=minz+40
c) Zc=minz+55
d) Zc=minz+70
e) Zc=minz+95
Fig. 9 a) 3D model of bunny

## Slide 18
Fig. 11:- Animation of tool path trajectory

## Slide 19
Fig. 10:- 3D representation of tool path lines

## Slide 20: FUTURE WORK
Optimization of an algorithm for slicing of STL file of the 3D object by reducing time-complexity.
Development of a method to represent the contour formation of each slice with the help of intersection points and normal vector information.

## Slide 21: THANK YOU